## Slide 1: Week 4: Hardware Logic + SQL Foundations
CST1100 – Introduction to Computer Systems Instructor

## Slide 2: Agenda
Why digital logic still matters in modern computing
Truth tables and core gate behaviors
From gates to adders: designing combinational circuits
SQL origin story and relational thinking
SQL syntax warm-up + lab expectations

## Slide 3: Warm-Up: Binary Refresh
Recall: bits, voltage thresholds, binary digits (0/1)
Encoding numbers and characters sets the stage for gates
Quick check-in: convert 13 to binary and hex

## Slide 4: Digital Logic Basics
Logic levels mapped to binary states (0 V vs. 5 V)
Physical implementations: transistors enabling gates
Deterministic outputs let us chain components safely

## Slide 5: Core Gates & Symbols
NOT (inverter), AND, OR – building blocks
Derived gates: NAND, NOR, XOR, XNOR
Each gate described by truth table and circuit symbol diagram

## Slide 6: Truth Tables
Enumerate all input combinations to verify behavior
Example: XOR outputs 1 only when inputs differ
Use tables to reason about larger circuits systematically

## Slide 7: Circuit Composition
Wiring outputs to inputs forms combinational logic
Propagation delay and fan-out considerations
Software simulations mirror hardware wiring

## Slide 8: Lab Part 1: Python Gate Simulator
Define gate functions that accept boolean/int inputs
Generate truth tables programmatically for quick validation
Build half-adder and full-adder from primitive gates
Stretch goal: ripple-carry adder using function composition

## Slide 9: Bridging to Data Layers
Hardware enables instruction execution and data storage
Operating systems and databases depend on reliable logic
Transition to abstracting data with relational models

## Slide 10: SQL Origins
Early 1970s: IBM System R, Edgar F. Codd and relational theory
SQL standardized by ANSI in 1986; vendors adopt dialects
Designed to query data declaratively, not procedurally

## Slide 11: Why SQL Still Matters
Portable knowledge across database systems
Foundation for analytics, app backends, and Supabase labs
Complements Python data pipelines you build in lab

## Slide 12: SQL Syntax Tour
CREATE TABLE defines schema (columns + types)
INSERT adds rows; SELECT retrieves filtered data
Clauses: WHERE, ORDER BY, LIMIT
Preview of joins to connect related tables next weeks

## Slide 13: Lab Part 2: SQLite Sandbox
Use Colab/Notebook sqlite3 module, no install required
Create components table, insert sample hardware items
Practice SELECT queries: filter by type, sort by price
Reflect on how SQL describes data relationships

## Slide 14: Team Extension Ideas
Log generated truth tables to CSV, load into Supabase
Visualize adder outputs with matplotlib for debugging
Document findings in lab README for portfolio credit

## Slide 15: Exit Ticket
One insight about hardware logic
One SQL command you can now write confidently
Questions to explore before next session